Setting up ROS packages in Robotware Yumi_6.03
- Prerequsites
- YuMi must have a static IP.
- If simulated, IP of the simulated machine must be changed in ROS_socket.sys	under ROS folder.
- Copy Ros folder under YuMi Home
- Load system parameters using SYS.cfg file. Once loaded you should see the below mentioned config in Robotstudio.

RobotStudio (RAPID):
- There will be 9 RAPID files in total: 3 .sys files (common, messages and socket, which are common to all tasks) and 6 .mod files (2 each of stateServer, motionServer and motion, 1 for each arm).
- Use the install server tutorial on https://wiki.ros.org/abb for reference as to how to install and run the server.
- Here's the configuration->controller setup:
  - Tasks:
Task	Type	TrustLevel	Use Mechanical Unit Group
MotionServer_left	SEMISTATIC	SysStop	rob_l
MotionServer_right	SEMISTATIC	SysStop	rob_r
StateServer_left	SEMISTATIC	NoSafety	rob_l
StateServer_right	SEMISTATIC	NoSafety	rob_r
T_ROB_L	NORMAL	N/A	rob_l
T_ROB_R	NORMAL	N/A	rob_r

- Automatic Loading of Modules:
File	Task	All Tasks
HOME:/ROS/ROS_common.sys		YES
HOME:/ROS/ROS_socket.sys		YES
HOME:/ROS/ROS_messages.sys		YES
HOME:/ROS/ROS_stateServer.mod	StateServer_left	NO
HOME:/ROS/ROS_stateServer_right.mod	StateServer_right	NO
HOME:/ROS/ROS_motionServer.mod	MotionServer_left	NO
HOME:/ROS/ROS_motionServer_right.mod	MotionServer_right	NO
HOME:/ROS/ROS_motion.mod	T_ROB_L	NO
HOME:/ROS/ROS_motion_right.mod	T_ROB_R	NO